## Slide 1: netduino
Boise Code Camp 2014
Scott Jeide
@ScottJeide

## Slide 2: Netdu-what?
Open Source HW Platform
.NET Micro Framework
Visual Studio
~$60

## Slide 3: What can it do?
Connectivity
USB
Ethernet
22 I/O pins
  Digital
  Analog
  UART
  PWM
Micro SD
Shields
HW Specs
32-bit 120MHz
384 KB ROM
100 KB RAM
5 V power

## Slide 4: Development Environment
Visual Studio 2010 (Express OK)
  Visual Studio 2012 (sort of)
Netduino SDK
.NET Micro Framework SDK
USB

## Slide 5: .NET Support!
CLR 1.0 / .NET 1.1 +
  IEnumerable
  Extension methods
  Yield
  Lambdas
Events
Timers
Threads
HttpWebRequest
Input/OutputPort
AnalogInput/Output
InterruptPort
Debug
Trace
Math

## Slide 6: Get On With It!

## Slide 7: Gottchas
No https
No xml/json parser
No string.Format
No generics (and no LINQ)

## Slide 8: Best Practices
using(…) and IDisposable are your friends
  Use SD card for large HttpWebResponses
Debug.EnableGCMessages(true);
Catch Exceptions
Make Main() a watchdog
  Do work in threads
Initialize pins – no floaters
Keep InterruptPorts in scope

## Slide 9: Helpful Links
www.netduino.com
http://www.netduino.com/downloads/gettingstarted.pdf
http://informatix.miloush.net/Microframework/Articles/CisFeatures.aspx
http://www.amazon.com/Getting-Started-Electronics-Forrest-Mims/dp/0945053282
http://msdn.microsoft.com/en-us/library/hh423649.aspx

## Slide 10: Thanks
Go Make Something!
Follow me @ScottJeide
Scott.Jeide@live.com
https://github.com/scottjeide/BCC-NetDuino